## Slide 1: Interlocking by curvature
그래픽스 및 기하처리 연구실
정보컴퓨터공학부 예기즈바에브 졸란

## Slide 2: Problem statement (139 words)
Given a closed genus-0 solid, partition it into k pieces that interlock in R³: no proper subassembly separates by translation except one designated key.
Elber's construction divides the parameter domain D of a trivariate M and maps each cell through M. If M is affine the cuts stay planar, and a planar partition always comes apart, so joints are the only resistance. We cut in D and let M curve the cuts. Two pieces sharing an interface S separate along d only if d·n ≥ 0 at every point of S; when the normals spread far enough, no such d exists and the pair is locked.
Criteria: interlocking verified in R³ (single key, then level k); Jacobian of M∘R positive everywhere; every piece one connected component above a minimum thickness; roughly uniform piece sizes; no joints exposed in cavities.
Problem statement
Notes: Scope for the first round: genus 0, no limbs, translation only.

## Slide 3: Two models from Elber's own script
Step 1 · Reproduce Elber, pins removed
Elber's puz_vol.irt (IRIT), copied as puz_vol - Copy.irt with every pin and hole deleted
PuzzleVolEarth: a sphere shell. PuzzleVolDuck: ruled between the duck surface and an inner core
Divided 2×2×2 in D: u around the axis, v along the profile, w through the thickness
Tiles at size 1.0 (Elber's 0.99 left room for pins); the trivariate M is saved next to the pieces
[Screenshot: GuIrit, PuzzleVolEarth and PuzzleVolDuck, pins removed]
Notes: Only these two models are used. Elber's grids are N×M×1; the professor asked for 2×2×2, which adds the radial cut w through the thickness.

## Slide 4: R is a randomization amount, not a radius
Step 3 · The R sweep
RandomizeInterior(TV, R): every interior control point += random(−R, R); the outer shape is unchanged
Random generator re-seeded before every R: each R scales one fixed field of offsets
Duck refined in depth first (it had only 2 control points across its thickness)
Rule: interior det J ≤ 0 → the map folds → the case is invalid and not ranked
model | valid R | folds from
sphere | 0 – 0.125 | 0.15
duck | 0 – 0.015 | 0.02
Elber's Earth, R = 0.2 | – | folds
Notes: Re-seeding makes the sweep one shape at several strengths. Folded cases are kept to show what folding does.

## Slide 5: Blocking pairs, immobilized pieces, single key
Step 4 · The table
Sphere (PuzzleVolEarth)
R | det J | blocking pairs | immobilized | single key
0 | 0.282 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.025 | 0.251 | none | 4 of 8 | no
0.05 | 0.222 | none | 4 of 8 | no
0.075 | 0.194 | 6–7 | 5 of 8 | no
0.1 | 0.168 | 6–7 | 5 of 8 | no
0.125 | 0.085 | 6–7 | 5 of 8 | no
0.15 | -0.092 folds | – | – | invalid
Duck (PuzzleVolDuck)
R | det J | blocking pairs | immobilized | single key
0 | 0.036 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.0025 | 0.036 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.005 | 0.036 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.0075 | 0.035 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.01 | 0.029 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.015 | 0.002 | 0–1, 2–3, 4–5, 6–7 | 8 of 8 | no
0.02 | -0.031 folds | – | – | invalid
No valid case has a single key. Duck: every piece is immobilized, but each piece and its radial partner slide out together. Sphere: R = 0 blocks only on a knife edge; at R = 0.025–0.05 all four outer shells come out alone (under 2° of clearance); from R = 0.075 pair 6–7 closes. Pairs 0–1, 2–3, 4–5, 6–7 = the two layers of one quarter (the radial cut). Controls: flat box 0 of 12 blocked; duck 2×2×1 (Elber's topology) 0 of 4 blocked.
Notes: Blocked or free is decided exactly by the clearance (distance from the origin to the convex hull of the face normals), not by sampling directions.

## Slide 6: Who blocks whom
Step 4 · The blocking graph
Sphere, R = 0.1
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  | · | · |  | · |  |  | 
1 | · |  |  | · |  | · |  | 
2 | · |  |  | · |  |  | · | 
3 |  | · | · |  |  |  |  | ·
4 | · |  |  |  |  | · | · | 
5 |  | · |  |  | · |  |  | ·
6 |  |  | · |  | · |  |  | B
7 |  |  |  | · |  | · | B | 
Immobilized: 0, 2, 4, 6, 7. Free alone: 1, 3, 5.
Duck, R = 0
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  | B | · |  | · |  |  | 
1 | B |  |  | · |  | · |  | 
2 | · |  |  | B |  |  | · | 
3 |  | · | B |  |  |  |  | ·
4 | · |  |  |  |  | B | · | 
5 |  | · |  |  | B |  |  | ·
6 |  |  | · |  | · |  |  | B
7 |  |  |  | · |  | · | B | 
Immobilized: 0, 1, 2, 3, 4, 5, 6, 7. Free alone: none.
B = blocked (no direction separates them) · = touching, can separate empty = not touching. Piece = 4·(u half) + 2·(v half) + (w layer)
Notes: Each piece touches three others. On the duck the radial neighbour always blocks, so every piece is immobilized, yet the pair moves out together through the flat cuts.

## Slide 7: The criteria, per R
Criteria
Sphere
R | det J positive | thinnest (3% limit) | largest / smallest | key / level k
0 | yes | 8.1% pass | 2.7 warn | no / 0
0.025 | yes | 6.0% pass | 2.8 warn | no / 0
0.05 | yes | 4.2% pass | 2.9 warn | no / 0
0.075 | yes | 2.7% fail | 3.0 warn | no / 0
0.1 | yes | 1.9% fail | 3.1 fail | no / 0
0.125 | yes | 0.5% fail | 3.2 fail | no / 0
0.15 | no (folds) | – | – | –
Duck
R | det J positive | thinnest (3% limit) | largest / smallest | key / level k
0 | yes | 0.2% fail | 11.4 fail | no / 0
0.0025 | yes | 0.2% fail | 11.4 fail | no / 0
0.005 | yes | 0.2% fail | 11.5 fail | no / 0
0.0075 | yes | 0.2% fail | 11.5 fail | no / 0
0.01 | yes | 0.2% fail | 11.5 fail | no / 0
0.015 | yes | 0.2% fail | 11.7 fail | no / 0
0.02 | no (folds) | – | – | –
One connected component: yes in every valid row (a piece is one box through a continuous map; only a fold could break it). Joints in cavities: not applicable, no joints in this experiment. Sizes: pass ≤ 2, warn ≤ 3.
Notes: The 3% thickness limit is a default, not a printing requirement.

## Slide 8: Each §6 item, matched to our plan
Elber 2025, §6 Future Work
§6 item | our step | evidence it is addressed
1 · Richer domain topologies (hexagonal prisms, general space-filling cells) | Later rounds: the analyser must not assume cuboid cells | The same table from a non-cuboid division of D
2 · Non-regular division + automatic (dis)assemblability ("herein we manually ensure that") | The core: translational DBG over freeform interfaces | The blocking table, computed not asserted (done)
3 · Better joints; joints exposed by deep cavities | Joints only where the DBG says faces are loose; cavities as a criterion | A joint moved off a cavity-reachable face, before / after
4 · Pin / hole sizes distorted by M | J is already computed: scale features by the local stretch | Joint sizes in R³ with and without compensation
Notes: Item 2 is the paper's own open problem - Elber ensures disassemblability manually - and it is exactly what this experiment automates.

## Slide 9: Open questions
Rotations? The d·n test covers straight pulls only. Proposal: translation only for the first paper, stated as a limitation, plus a swept-volume check on the final design
Which shapes? Proposal: genus 0, no limbs (deformed sphere, simple busts; not the torus or armadillo). Is "no limbs" about genus, the medial axis, or convex cross-sections? It needs an operational test
Is random R the right instrument? It folds the duck at 0.02 and never makes the u / v cuts block. Design the curvature instead (wavy cuts in D, harmonic trivariate)?
Which level k? Song 2012 (unique key at each step) is computed; Chen 2022 (moves before the first piece comes free) needs motion search
What do joints become? If curvature does not lock, the DBG says which faces are loose: fewest joints, or least visible?
Fitted or constructed trivariates, and a thickness limit in mm?
Open questions